## Slide 1: MLFSOM Simulations Homogeneous Beam (mosaicity turned off)

## Slide 2
MLFSOM input parameters
Crystal & Exp. Params | 
Protein | Tetragonal lyosyzme
PDB code | 1H87
Unit cell | 77.25, 77.25, 38.66
Detector | Pilatus 6M
Mosaicity (initial-final) | 0.15o (does not change)
B-factor (initial-final) | 14.8 – 51.8 A2
Fractional unit cell change | 1% (at the end)
Initial resolution | 1.5 A
Oscillation (stills) | 0.01o
Number of frames | 20
Beam Params | 
Beam size | 100 micron
Crystal size | 77.8 micron
Wavelength | 1.0 A
Beam dispersion | 0.00014
Beam divergence (hor, ver) | (0.06o, 0.01o)
Exposure per frame | 0.5 sec
Beam flux | 8.4 x 1010 ph/sec
Mosaicity is set to 0.15 and it is the same for each frame

## Slide 3
Integrated intensity
Monotonic and very regular decay compared to the simulation with the mosaicity
No increase or lag in the intensity at the beginning

## Slide 4
Integrated intensity by resolution shells
More regular decay

## Slide 5
Half-dose vs. resolution
Seems like obeying the d2 law. I need to increase the max resolution and get better stats though.

## Slide 6
OBSERVATIONS & NOTES
This simulation is again at 1.5 A resolution. It is better to go for higher res i.e. 1.1-1.2 A which improves stats significantly.